## Slide 1: EXPERIMENT Interfacing switch and button with Intel Galileo Gen 2 and ring the buzzer when switch is pressed
Zeenat Shareef, PhD Scholar
Department of Computer Science
IGDTUW

## Slide 2
INTRODUCTION
REQUIREMENTS
In this experiment, we will send ring the sensor when switch is pressed.
HARDWARE:
Intel Galileo Gen 2
Power Cable
USB cable
Base shield of grove kit
Switch of grove kit
buzzer of grove kit
SOFTWARE:
Arduino1.5.3-Intel.1.0.4
Intel Galileo driver
GROVE SWITCH
GROVE BUZZER

## Slide 3
INTERFACING DIAGRAM
SWITCH
BUZZER
BASE SHIELD-GROVE KIT
GND
VCC
NC
OUTPUT
GND
VCC
NC
OUTPUT

## Slide 4
WORKSHOP ON INTEL IOT / 19.03.2016
CODE
int buz = 3;
int but=4;
void setup()
{
pinMode(buz, OUTPUT);
pinMode(but, INPUT);
}
void loop()
{
int sensorValue = digitalRead(4);
if(sensorValue == 1)
digitalWrite(buz,HIGH);
else
digitalWrite(buz,LOW);
}

## Slide 5
OUTPUT and SCREENSHOTS
ACTUAL DEPLOYMENT
buzzer
Button